## Slide 1
MR FIT
AI-Powered Fitness Tracker
Real-time exercise classification & repetition counting
from wearable IMU sensor data
Ahmed Elawady • Mansoura University • Faculty of Computers & Information • 2026
98.7% · Accuracy
5 · Exercises
<5ms · Latency
Notes: Open: 'My name is Ahmed. This is MR Fit — an AI system that knows what exercise you're doing before you tell it.' Pause. Let the title breathe.

## Slide 2
Imagine you are at the gym with no coach watching you. You don't know if you are doing your exercises correctly. You lose count of your repetitions. You have no feedback at all. MR Fit solves exactly this problem. It is an AI-powered system that reads your body movement through a small sensor, recognizes your exercise automatically, and counts your repetitions in real time — all without you pressing a single button.

## Slide 3
ROADMAP
Presentation Agenda
01
Problem & Motivation
Why we built MR Fit
02
System Architecture
5-layer pipeline overview
03
Hardware Layer
ESP32, MPU-6050, OLED display
04
Data Pipeline
Ingestion, cleaning, preprocessing
05
Feature Engineering
50+ features from 6 raw axes
06
Model Training
5 classifiers, 4 feature sets
07
API & Integration
FastAPI server & endpoints
08
Results & Evaluation
Accuracy, latency, rep counting
09
Tech Stack
Full project file structure
10
Conclusion & Roadmap
What's next for MR Fit
Notes: Give audience a map of the talk. Say: 'We'll move from the problem, through every layer of the system, and end with our results and what comes next.'

## Slide 4
WHY DID WE BUILD THIS?
The Problem
?
People train without real-time feedback on form or reps
Manual rep counting breaks focus and concentration
Personal coaches are expensive and not always accessible
Existing wearables are costly, closed-source, or inaccurate
Notes: Ask the committee: 'How many of you have lost count of your reps at the gym?' Let it land. Then say: 'These four problems motivated MR Fit.'

## Slide 5
SOLUTION
MR Fit — One Sentence
"Wear the sensor. Start your workout. MR Fit does the rest."
Detects Exercise
Bench press, squat, row,
overhead press, deadlift
Counts Reps
Peak detection on filtered
magnitude signal
Real-Time
Under 5ms from sensor
reading to prediction
Low-Cost HW
ESP32 + MPU-6050
< $10 in total hardware
Fully Offline
No cloud, no internet
needed — runs local
Open Pipeline
Modular Python code,
FastAPI, Docker-ready
Notes: Say: 'MR Fit is the answer to all four problems. Let me walk you through how it works from sensor to prediction.'

## Slide 6
SYSTEM DESIGN
System Architecture
1
IMU Sensor
ESP32 + MPU-6050
6-axis @ 5 Hz
▶
2
Preprocessing
Outlier removal
+ Butterworth LPF
▶
3
Feature Engine
50+ features
PCA · FFT · KMeans
▶
4
Random Forest
98.7% accuracy
5 exercise classes
▶
5
FastAPI
REST API
< 5ms latency
sensor_handler.py → preprocessing.py → feature_engineering.py → predict.py → app.py
Notes: Walk left to right. Every arrow is a function call in Python. The whole pipeline runs in under 5ms.

## Slide 7
HARDWARE
Hardware Components
ESP32 Microcontroller
Main processing unit
Dual-core 240 MHz
Built-in WiFi + Bluetooth
UART, I²C, SPI support
Flash: 4MB, RAM: 520KB
Sends data to FastAPI via serial
MPU-6050 IMU Sensor
Motion capture chip
3-axis accelerometer ±2g–±16g
3-axis gyroscope ±250–±2000°/s
16-bit ADC per axis
I²C address 0x68
Sampling at 5 Hz (200ms interval)
SSD1306 OLED Display
Real-time feedback
128×64 pixel display
Shows: exercise name
Shows: rep count
Shows: confidence %
I²C bus — same as MPU-6050
Notes: Explain: 'Three chips. The MPU reads motion, the ESP32 is the brain, the OLED shows feedback instantly on the device.'

## Slide 8
DATA & CONFIG
Configuration & Data Ingestion
config/config.py
SAMPLING_FREQ = 5.0 # Hz
WINDOW_SIZE = 5 # samples
N_CLUSTERS = 5 # KMeans
TEST_SIZE = 0.20 # 80/20 split
RANDOM_STATE = 42
EXERCISES = [
"bench", "squat", "row",
"ohp", "dead"
]
REP_CUTOFFS = {
"bench": 0.40, # Hz
"squat": 0.35,
"row": 0.45,
"ohp": 0.38,
"dead": 0.30
}
data/loader.py
def load_dataset(path):
df = pd.read_csv(path)
# Extract labels from filename
# e.g. A-bench-medium-5.csv
# → exercise='bench', set=5
df = merge_sensor_axes(df)
df = resample_to_200ms(df)
return df
def load_for_inference(json_data):
df = pd.DataFrame([json_data])
validate_columns(df)
return df
Notes: config.py is the single source of truth. If you change SAMPLING_FREQ here, it propagates everywhere. loader.py handles both CSV (training) and JSON (live API).

## Slide 9
DATA PREPROCESSING — STEP 1
Outlier Removal
Chauvenet's Criterion
For each column and each exercise label:
1. Compute μ (mean) and σ (std deviation)
2. Calculate Z-score for each value
3. If P(|Z| ≥ z) < 1/(2N) → outlier
4. Replace outlier with NaN
5. Linear interpolate to fill NaN gaps
✓ More statistically sound than IQR method
✓ Adapts threshold to sample size N
Before → After
Before (noisy signal):
↑ Outliers circled
After (clean + interpolated):
Notes: Key: Chauvenet adapts to sample size N. For N=1000, the threshold is different than N=100. This is why it outperforms static IQR-based removal.

## Slide 10
PREPROCESSING — STEP 2
Butterworth Low-Pass Filter
What is it?
A digital filter that removes high-frequency noise from the sensor signal. Only frequencies below the cutoff pass through. Implemented with scipy.signal.butter + filtfilt.
Why Butterworth?
Maximally flat magnitude response in the passband — no ripple. filtfilt applies it forward AND backward to eliminate phase shift, preserving timing of movements.
Cutoff Frequency
Set to 0.1× Nyquist frequency by default. Nyquist = 5Hz/2 = 2.5Hz. Cutoff = 0.25Hz for noise removal. Rep-counting uses per-exercise cutoffs (0.30–0.45 Hz).
preprocessing.py — LowPassFilter
def apply_lowpass(df, col, cutoff_freq, sampling_freq, order=5):
nyquist = sampling_freq / 2 # 2.5 Hz
normal_c = cutoff_freq / nyquist # normalise to [0,1]
b, a = butter(order, normal_c, btype='low') # design filter
df[col] = filtfilt(b, a, df[col].values) # zero-phase apply
return df
Notes: Emphasize filtfilt: 'We apply the filter twice — forward and backward. This doubles the effective order and removes phase lag, so peak positions are accurate for rep counting.'

## Slide 11
FEATURE ENGINEERING
6 Inputs → 50+ Features
RAW
INPUT
acc_x
acc_y
acc_z
gyro_x
gyro_y
gyro_z
▶
1
Magnitude
acc_r = √(acc_x²+acc_y²+acc_z²)
gyro_r = √(gyro_x²+gyro_y²+gyro_z²)
2 features
2
PCA
sklearn PCA(n_components=3)
Fit on all 6 axes together
3 features
3
Temporal
Rolling window of 5 samples
mean + std per channel
12 features
4
Frequency (FFT)
abs(rfft) amplitudes per channel
spectral entropy per channel
24+ features
5
KMeans Cluster
KMeans(k=5) on acc_x/y/z
cluster label as categorical
1 feature
Total: 50+ features per reading → ready for classification
Notes: This slide is the technical heart of the talk. Say: 'We don't feed raw numbers to the model. Each of these transformations helps the model distinguish one exercise from another.'

## Slide 12
FEATURE ENGINEERING
Feature Set Progression (f_set_1 → f_set_4)
f_set_1
acc_x, acc_y, acc_z
gyro_x, gyro_y, gyro_z
RF Accuracy: 91%
6 features
f_set_2
All f_set_1
acc_r (magnitude)
gyro_r (magnitude)
pca_1, pca_2, pca_3
RF Accuracy: 94%
11 features
f_set_3
All f_set_2
acc_x_temp_mean
gyro_z_temp_std
...12 temporal features
RF Accuracy: 96.5%
23 features
f_set_4
All f_set_3
FFT amplitudes × 6 channels
Spectral entropy × 6
KMeans cluster label
RF Accuracy: 98.7%
50+ features
Each feature set builds on the previous. We evaluated all four to find the best model-feature combination.
Notes: Say: 'We built four progressive feature sets. Each adds more information. The final set — f_set_4 — gives us 98.7% accuracy.'

## Slide 13
FEATURE ENGINEERING — REP DETECTION
Repetition Counting
How Reps Are Counted
Step 1
Compute acc_r = √(acc_x²+acc_y²+acc_z²)
Step 2
Apply low-pass filter (per-exercise cutoff Hz)
Step 3
Detect local maxima via scipy.signal.argrelextrema
Step 4
Each peak = 1 complete repetition
Step 5
Return count + timestamps
Per-Exercise Cutoff Frequencies:
bench:0.40Hz · squat:0.35Hz · row:0.45Hz · ohp:0.38Hz · dead:0.30Hz
Magnitude Signal — Bench Press
✓
✓
✓
Peak = 1 Rep ✓ ×3 peaks = 3 reps
Mean Absolute Error: < 1 rep
Validated across 5 exercise classes, multiple set sizes
Notes: The gold bars are detected peaks. Each peak is one rep. The MAE under 1 rep is a strong result — it means the counter is almost always exactly right.

## Slide 14
MODEL TRAINING
Training Pipeline — train.py
3
Feature Engineering
Apply full 5-stage
feature pipeline
▶
2
Preprocess
Chauvenet + Interpolation
Butterworth LPF
▶
1
Load Dataset
All CSVs from data/raw/
Labels from filenames
▼
4
Split 80/20
train_test_split
stratified by label
▶
5
GridSearchCV
5-fold CV
hyperparameter tuning
▶
6
Evaluate & Save
Compare all models
Save best pkl
Notes: main.py --train triggers this full pipeline. It takes ~2 minutes on CPU. The result is three saved artifacts in saved_models/.

## Slide 15
MODEL COMPARISON
Why Random Forest Won
Algorithm | f_set_1 | f_set_2 | f_set_3 | f_set_4 ✓ | Train Time | GPU Needed
Random Forest ✅ | 91% | 94% | 96.5% | 98.7% | ~2 min | No
Neural Network | 87% | 91% | 94.0% | 97.2% | ~45 min | Preferred
KNN | 83% | 88% | 92.0% | 95.1% | ~3 min | No
Decision Tree | 80% | 83% | 88.0% | 91.3% | <1 min | No
Naive Bayes | 72% | 76% | 81.0% | 84.0% | <1 min | No
GridSearchCV (5-fold CV) used for all models · Best params: n_estimators=200, max_depth=None, min_samples_split=2
Notes: Random Forest wins on three fronts: accuracy, training time, and no GPU requirement. This is the right choice for a production system that might run on a Raspberry Pi.

## Slide 16
MODEL ARTIFACTS
What Gets Saved After Training
random_forest_model.pkl
The trained Random Forest classifier.
Loaded at startup for all predictions.
Contains 200 decision trees.
joblib.dump(model, 'random_forest_model.pkl')
feature_pipeline.pkl
The full sklearn Pipeline:
StandardScaler + PCA + KMeans.
Fit on training data only.
joblib.dump(pipeline, 'feature_pipeline.pkl')
feature_set.pkl
List of 50+ feature column names
in exact order the model expects.
Prevents column mismatch errors.
joblib.dump(feature_cols, 'feature_set.pkl')
⚠ Rule: The pipeline and feature_set must always come from the SAME training run as the model — never mix versions.
Notes: This is a critical design decision. Three artifacts, always together. If you retrain the model you must also retrain and resave the pipeline.

## Slide 17
MODEL INFERENCE
Real-Time Inference — predict.py
models/predict.py — Predictor.predict()
def predict(self, sensor_reading: dict):
df = load_for_inference(sensor_reading)
# Apply full feature pipeline
df = self.pipeline.transform(df)
# Keep only trained feature columns
X = df[self.feature_cols]
# Classify
label = self.model.predict(X)[0]
proba = self.model.predict_proba(X)[0]
conf = max(proba)
# Count reps
reps = count_reps(df, label)
return {
"exercise": label,
"confidence": round(conf, 3),
"rep_count": reps,
"proba_all": dict(zip(EXERCISES, proba)),
"latency_ms": round(elapsed*1000, 2)
}
Example JSON Response
{
"exercise": "bench",
"confidence": 0.947,
"rep_count": 7,
"proba_all": {
"bench": 0.947,
"squat": 0.031,
"row": 0.012,
"ohp": 0.007,
"dead": 0.003
},
"latency_ms": 4.2
}
Notes: The key output fields: exercise name, confidence, rep count, all class probabilities, and latency. The OLED display shows exercise + reps + confidence.

## Slide 18
API LAYER
FastAPI Server — app.py
POST
/predict
Single IMU reading → classification + reps
{"acc_x":0.1,"acc_y":-9.7,"acc_z":0.3,
"gyro_x":0.02,"gyro_y":-0.01,"gyro_z":0.00}
POST
/predict/batch
Array of readings processed at once
{"readings": [...]}
GET
/health
Returns model status + uptime
→ {"status":"ok","model":"loaded"}
GET
/model/info
Returns model name, accuracy, feature count
→ {"model":"RandomForest","accuracy":0.987}
Deployment: docker-compose up → FastAPI served on port 8000 · uvicorn with 4 workers · Health check every 30s
Notes: The API is stateless. Each request is independent. This makes horizontal scaling trivial with Docker Compose.

## Slide 19
SYSTEM INTEGRATION
End-to-End Data Flow
MPU-6050
Reads 6-axis at 5Hz
▶
ESP32
Packages JSON via UART
▶
sensor_handler
Abstracts HW mode
▶
POST /predict
FastAPI receives reading
▶
pipeline.transform
50+ features built
▶
RF.predict
Label + confidence + reps
▶
JSON response
< 5ms total latency
▶
OLED display
Shows result to user
Latency Breakdown
Sensor read
~50ms
UART transfer
~10ms
Feature build
~2ms
RF inference
~1.5ms
JSON response
~0.5ms
Live output: exercise="bench" | confidence=0.947 | reps=7 | latency=4.2ms
Notes: This is the full pipeline in one slide. Memorize the timing breakdown — the committee will ask about latency.

## Slide 20
RESULTS
Classification Results
98.7%
Overall Accuracy
<5ms
Latency
<1 rep
Rep Count MAE
5
Exercise Classes
Chart: 
| Bench Press | Squat | Barbell Row | Overhead Press | Deadlift
Accuracy (%) | 99 | 98 | 98 | 97 | 99
Notes: All five exercises exceed 97%. Overhead press at 97% is the lowest — it shares motion patterns with bench press, which makes it slightly harder to distinguish.

## Slide 21
MODEL EVALUATION
Confusion Matrix
Predicted →
Actual ↓
bench
bench
99%
0%
0%
1%
0%
squat
squat
0%
98%
1%
0%
1%
row
row
0%
1%
98%
1%
0%
ohp
ohp
2%
0%
1%
97%
0%
dead
dead
0%
1%
0%
0%
99%
Legend
Correct
Misclass.
Zero
⚠ ohp ↔ bench: 3% confusion — both involve horizontal pushing motion. Addressed by temporal + FFT features distinguishing range of motion.
Notes: The confusion between OHP and bench is expected — they're biomechanically similar. The FFT features help because OHP has a different frequency profile.

## Slide 22
TECH STACK
Project File Structure
📁 fitness_tracker/
— Project root
📄 main.py
— Entry point — --train / --serve / --stream / --evaluate
📁 config/
📄 config.py
— All constants: SAMPLING_FREQ, EXERCISES, REP_CUTOFFS
📁 data/
📄 loader.py
— CSV → DataFrame and JSON → DataFrame for inference
📄 preprocessing.py
— Chauvenet outlier removal + Butterworth LPF
📁 features/
📄 feature_engineering.py
— Full 5-stage pipeline: magnitude, PCA, temporal, FFT, KMeans
📁 models/
📄 train.py
— GridSearchCV training of 5 classifiers × 4 feature sets
📄 predict.py
— Predictor class for real-time inference + rep counting
📄 model_utils.py
— save_model() and load_model() with joblib
📁 api/
📄 app.py
— FastAPI server with 4 endpoints
📁 hardware/
📄 sensor_handler.py
— SimulatedSensor / SerialSensor / GPIOSensor
📁 saved_models/
— random_forest_model.pkl · feature_pipeline.pkl · feature_set.pkl
📁 utils/
— helpers.py — logging and utility functions
📄 Dockerfile
— Container definition for deployment
📄 docker-compose.yml
— Service orchestration — API + health checks
Notes: Every folder has a single responsibility. config/ owns constants. data/ owns loading. features/ owns transformation. models/ owns training and inference. This separation makes the code testable.

## Slide 23
TECH STACK
Full Technology Stack
Machine Learning
scikit-learn (Random Forest, PCA, KMeans)
numpy · pandas
scipy (Butterworth filter, peak detection)
joblib (model serialization)
API & Backend
FastAPI (REST endpoints)
uvicorn (ASGI server)
pydantic (request validation)
Python 3.10+
Hardware
ESP32 (Espressif)
MPU-6050 (6-axis IMU)
SSD1306 (OLED 128×64)
pyserial / smbus2
DevOps
Docker + docker-compose
GitHub (version control)
pytest (unit tests)
logging (rotating file handler)
Notes: All open source. No paid cloud services. The entire system can be reproduced with pip install + docker-compose up.

## Slide 24
PROJECT CHALLENGES
Challenges We Faced
Single-row LPF failure
Applied minimum window check — skip filter if fewer than filter_order+1 samples in input.
Duplicate raw data files
Added deduplication in loader.py — sort by timestamp, drop duplicate firmware versions.
Pandas epoch/datetime bug
Replaced int-based epoch parsing with pd.to_datetime() + explicit timezone handling.
Feature column mismatch
feature_set.pkl enforces exact column list and order at inference time.
ESP32 WiFi firewall block
Switched to UART serial connection — more reliable, zero network dependency.
Notes: The committee often respects honesty about challenges more than a perfect-sounding project. These show real engineering judgment.

## Slide 25
RELATED WORK
MR Fit vs Existing Solutions
Feature | MR Fit | Apple Watch | Fitbit Charge | Academic Papers
Exercise Detection | 5 classes (98.7%) | Limited, closed | Steps only | Varies (60–95%)
Rep Counting | Auto (<1 MAE) | Manual input | Not supported | Rarely included
Real-time (<5ms) | ✓ Yes | Network delay | No API | Offline only
Open Source | ✓ Fully open | Closed | Closed | Code rarely shared
Cost | <$10 hardware | $399+ | $129+ | Lab equipment
Offline | ✓ No cloud | Partial | Partial | Varies
MR Fit is the only open-source, sub-$10, offline solution with automatic exercise detection AND rep counting.
Notes: If the committee asks why not just use an existing product: cost, openness, and rep counting. MR Fit does things commercial products don't.

## Slide 26
CONCLUSION
What MR Fit Delivers
Delivered ✓
Real-time exercise classification — 98.7%
Automatic rep counting — MAE < 1 rep
Production FastAPI server — < 5ms
Modular hardware (ESP32 / RPi / Simulated)
Full ML pipeline — open source + Docker
Confusion matrix + per-class evaluation
Future Roadmap 🚀
Mobile app (iOS & Android)
Cloud dashboard + analytics
Form correction (joint angles)
Deep learning for 20+ exercises
Heart rate + fatigue monitoring
Multi-user gym deployment
MR Fit — Mansoura University, Faculty of Computers & Information · 2026 · Ahmed Elawady
Notes: Close with: 'MR Fit is not a prototype. It is a production-ready system built from scratch. Thank you — I am happy to answer any questions.'

## Slide 27
Thank You
Questions & Discussion
Ahmed Elawady · binel3wady@gmail.com · github.com/AhmedElawady8
Mansoura University · Faculty of Computers and Information · AI Engineering · 2026
MR Fit · github.com/AhmedElawady8/MRFIT_Smart_Exercise_Tracker
Notes: Stay calm. Smile. If you don't know an answer, say: 'That's a great point — we noted it as future work.' Never guess on a number you're not sure about.